ACPI in Linux
ACPI in Linux
Len Brown
len.brown@intel.com
July 20, 2005

---
Agenda
Agenda
ACPI Tutorial/Decoder-Ring
What changed in the last year?
ACPI 3.0
What's next?

---
ACPI Tables
RSDP – Root System Description Pointer
RSDT – Root System Description Table
FADT – Fixed ACPI Description Table
DSDT – Differentiated System Description Table
SSDT – Secondcary System Description Table
SRAT – System Resource Affinity Table
SLIT – System Locality Distance Inf. Table

---
ACPI Configuration
Replaces Legacy configuration standards and proprietary methods
Enumerates Motherboard devices:
  - Processor
  - Memory
  - I/O devices
  - Interrupts
  - Hot Plug
ACPI comes with the BIOS – it does not know anything about add-in devices.
ACPI augments, but does not replace PCI config.

---
States
G0 (S0)
Working
G1 - Sleeping
C1 - idle
C0 - Execute
C3 - idle
C2 - idle
Throttling
P-states
S1 - Standby
S4 - Hibernate
S3 - Suspend
G2 (S5) –
Soft off
G3 – Mech off
Legacy
ACPI States

---
System Sleep S-States
S0 = Executing
S1 = Standby
S3 = Suspend to RAM
S4 = Suspend to Disk
S5 = Soft Power-off

---
C-States – CPU Idle Power States
Only C0 executes instructions
C1 – Cn do no execute instructions
Deeper C-states save more power cost more latency
/proc/acpi/processor/*/power

---
Processor Performance P-States
P0 = full MHz (and voltage)
P1 ... Pn = progressively lower MHZ and Volts
Different platforms offer different states
/sys/devices/system/cpu/cpu0/cpufreq
speedstep-centrino, acpi-cpufreq, cpufreq-stats

---
Throttling T-states
~Lineary power savings w/ Mhz
Older system had only throttling to manage processor performance.
P-states used for modern hardware, with T-states used only for thermal emergencies.
cpufreq sub-system can use only 1 method at a time. eg. p4-clockmod vs cpufreq-acpi
ACPI in addition to hardware guards TM1/TM2

---
Processor Power Saving Example

---
D0-D3
Device D-States
D0 – full on
D3 – full off
vs. PCI Power Management
Semanntics are device-class specific
Linux just starting to use ACPI D-states

---
Events
ACPI Events
System Control Interrupt (SCI)
  - Fixed Feature Events (FF)
  - General Purpose Events (GPE)
  - /proc/acpi/event

---
Linux/ACPI Deployment
This year the major Linux distributors are all shipping with ACPI built-in and enabled-by-default on all ACPI capable architectures (i386, x86_64, ia64)

---
Architecture
ACPI Tables
Platform BIOS, Firmware
Platform Hardware
ACPI Registers
ACPI BIOS
ACPICA Core
Linux/ACPI
acpid
/proc/acpi
User
Kernel
OSL
Button
Processor
Battery
AC
Thermal
Fan
ACPI Specification
Platform Defined

---
Bugzilla

---
New bugs/week

---
Linux/ACPI changes in past year
Linux PNP = PNPACPI, PNPBIOS, PNPISA
Hot Plug CPU, Memory
SMP Deep C-states
SMP S3/S4 progress
video control progress
hot-key progress
ACPICA Interpreter progress

---
A
ACPI Specification history
1996 ACPI 1.0
2000 ACPI 2.0
2004 ACPI 3.0

---
Drv
Device Drivers vs. Power Management
Devices need to recognize when idle and take power saving action.
Device drivers should not have to care if power management is handled by PCI-PM or ACPI.
Today, no connection between (conventional) motherboard device drivers and ACPI for resources or power management.

---
Policy
Linux need Power Policy Mgr
User specifies policy
manager communicates it to devices and sub-systems

---
do1
Configuration Todo
Fix device tree
Abstract Device Enumeration:
  - PCI/ACPI/Legacy resources
Docking Station support -

---
do2
Power Management Todo
Suspend/Resume reliability++
Abstract Device power states
  - PCI/ACPI D-states
System Power policy manager
C-states: tick timer stop in idle
Hot Keys ++

---
References
http://www.acpi.info
http://acpi.sourceforge.net